## Slide 1: Data-driven identification of a one-link robot with flexible joint
Course: Robotics 2
Professor: Alessandro De Luca
Tutor: Pietro Pustina
Students: Lorenzo Cirillo 1895955, Claudio Schiavella 1884561
Lagrangian Neural Network applied to elastic robots
Master in Artificial Intelligence and Robotics

## Slide 2
INTRODUCTION
Robot dynamic model
  Relationship between applied forces and motion
  D’Alembert, Hamilton
Euler-Lagrange equations
  Modeling and control
  Symbolic form equations of motions
Modeling systems Neural networks Lagrangian NN

## Slide 3
PARAMETRIC LAGRANGIAN
Lagrangian
Kinetic and potential energy
Generalized coordinates
  = robot DOF
Euler-Lagrange equations
Non-conservative forces
  Considered null in our application

## Slide 4
PARAMETRIC LAGRANGIAN
Parametric Lagrangian
Lagrangian analytical expression not always known
Alternative approach
  Learning L + Automatic differentiation

## Slide 5
RIGID ROBOT
Dynamic Model:
Acceleration:
Coriolis and Centrifugal term not present
  One single link
  Contribute to the joint when it is moving is null
1R robot with y-axis agreeing with gravity

## Slide 6
ELASTIC ROBOT
Dynamic model:
Accelerations:
Again Coriolis and Centrifugal term not present
  Constant inertia matrix
1R robot with y-axis agreeing with gravity

## Slide 7
BASELINE NN
Classic feedforward neural network
  Only fully connected layers
Learn directly from and
  Not considering Lagrangian and relative constraints
Function of a comparison baseline
  Same structure of Lagrangian NN to comparison reasons

## Slide 8
LAGRANGIAN NN
Same baseline structure, completely different approach
  Very close to robot nature
Learn Lagrangian
  Functional programming context
  Predictions benefit of the Lagrangian approach features
obtained from parametric Lagrangian

## Slide 9
SIMULATIONS
Type 1: Observe behavior of the two networks
  Trajectory tracking
  Trajectory error
  Energy conservation
Type 2: Introduce noise
  Same tests as in type 1
  Highlight network robustness in not ideal context

## Slide 10
RIGID CASE
Robot parameters
Network setup
Parameter | Measure
Length | 
Base radius | 
CoM distance | 
Mass | 
Inertia | 
Parameter | Measure
Length | 
Base radius | 
CoM distance | 
Mass | 
Inertia | 
Characteristic | Value
Layers | 4
Neurons | 500
Activation | Softplus
Loss | MSE
Regularization | L2 penalty
Train epochs | 10 000

## Slide 11
RIGID CASE – NETWORK TRAINING
Train and test losses

## Slide 12
RIGID CASE – SIMULATION 1
Initial conditions:

## Slide 13
RIGID CASE – SIMULATION 1

## Slide 14
RIGID CASE – SIMULATION 2
Initial conditions:

## Slide 15
RIGID CASE – SIMULATION 2

## Slide 16
RIGID CASE – SIMULATION 3
Initial conditions:

## Slide 17
RIGID CASE – SIMULATION 3

## Slide 18
ELASTIC CASE
Motor parameters
Network setup
Parameter | Measure
Height | 
Base radius | 
Mass | 
Reduction ratio | 
Inertia | 
Stiffness constant | 
Parameter | Measure
Height | 
Base radius | 
Mass | 
Reduction ratio | 
Inertia | 
Stiffness constant | 
Configuration | Units | Layers
A | 300 | 2
B | 500 | 4
C | 700 | 5

## Slide 19
ELASTIC CASE – CONFIGURATION A
Train and test losses

## Slide 20
ELASTIC CASE – SIMULATION 1
Initial conditions:

## Slide 21
ELASTIC CASE – SIMULATION 1

## Slide 22
ELASTIC CASE – SIMULATION 2
Initial conditions:

## Slide 23
ELASTIC CASE – SIMULATION 2

## Slide 24
ELASTIC CASE – CONFIGURATION B
Train and test losses

## Slide 25
ELASTIC CASE – SIMULATION 3

## Slide 26
ELASTIC CASE – SIMULATION 4

## Slide 27
ELASTIC CASE – CONFIGURATION C
Train and test losses

## Slide 28
ELASTIC CASE – SIMULATION 5

## Slide 29
ELASTIC CASE – SIMULATION 6

## Slide 30
CONCLUSIONS
At least in the rigid case, LNN performances are very good
  Both in trajectory error and energy conservation
Unfortunately, bad results in elastic case
Elastic LNN seems to improve as network complexity increase
  More wide/deep network and more initial conditions
  High computational resources needed
Paper LNN approach works on unitary configurations
  We reject this in preference to real robot parameters

## Slide 31
THANK YOU FOR THE ATTENTION